## Slide 1: EECS 489 Computer Networks Winter 2025
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Logistics
You’re ONLY allowed one double-sided 8.5in x 11in note sheet
  Basic calculators are allowed but you won’t need it

## Slide 3: General guidelines (1)
Test only assumes material covered in lecture, discussion sections, quizzes, and assignments
  Text: only to clarify details and context for the above
The test doesn’t require you to do complicated calculations
  Use this as a hint to determine if you’re on right track
You don’t need to memorize anything
You do need to understand how things work

## Slide 4: General guidelines (2)
Be prepared to:
  Weigh design options outside of the context we studied them in
  Contemplate new designs we haven’t covered in detail but can be put together
    e.g., I introduce a new IP address format; how does this affect..”
  Reason from what you know about the pros/cons of solutions we did study

## Slide 5: General guidelines (3)
Exam format
  MCQ questions
  Networking use cases
    Questions not ordered in terms of complexity

## Slide 6: General guidelines (4)
75-minute midterm exam
  Friday, Feb. 21 from 7PM - 8:30PM
    Room assignments (by the first two letters of your uniqname) are as follows:
      AA - DB: Chrysler 133
      DC - ZZ: Chrysler 220
  SSD accommodations
    Friday, Feb. 21 from 6PM at DOW 2150
  Other conflicts
    You have received separate emails by now

## Slide 7: What’s covered in the midterm?
Lectures: 1—9 (Up to “More Congestion Control”)
Assignments: 1
Discussion sections: 1—6 (Content related to lectures 1—9 and assignment 1)

## Slide 8: This review
Walk through what you’re expected to know at this point: key topics, important aspects of each
Not covered in review does NOT imply you don’t need to know it
  But if it’s covered today, you should know it
Summarize, not explain
  Stop me when you want to discuss something further!

## Slide 9: Topics
Basics (lectures 1–2)
Application layer (lectures 3–5)
  HTTP, DNS, CDN, Video Streaming, and Cloud
Transport layer (lectures 6–9)
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only

## Slide 10: Basic concepts
You should know:
  Packet vs. circuit switching
  Statistical multiplexing
  Link characteristics
  Packet delays

## Slide 11: Switched networks
End-systems and networks connected by switches instead of directly connecting them
Allows us to scale
  For example, directly connecting N nodes to each other would require N2 links!

## Slide 12: Two approaches to sharing
Packet switching
  Network resources consumed on demand per-packet
  Admission control: per packet
Circuit switching
  Network resources reserved a priori at “connection” initiation
  Admission control: per connection

## Slide 13: Statistical multiplexing
Allowing more demands than the network can handle
  Hoping that not all demands are required at the same time
  Good for bursty traffic (average << peak demand)
  Packet switching exploits statistical multiplexing better than circuit switching

## Slide 14: Delay
Consists of four components
  Transmission delay
  Propagation delay
  Queuing delay
  Processing delay
due to link properties
due to traffic mix and
switch internals

## Slide 15: End-to-end delay
transmission
propagation
queueing
processing
transmission
propagation
queueing
processing
transmission
propagation
We only consider store-and-forward in this class

## Slide 16: What we want
http://123.xyz
123.xyz server

## Slide 17: (Some of) What happens…
5.6.7.*
host
host
host
...
5.6.7.8
1.2.3.*
host
host
DNS
...
router
router
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 18: (More of) What happens
5.6.7.*
host
host
host
...
5.6.7.8
1.2.3.*
host
host
DNS
...
router
router
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 19: What we get
http://123.xyz
123.xyz server
Hello

## Slide 20: Layers
Layer: a part of a system with well-defined interfaces to other parts
One layer interacts only with layer above and layer below
Two layers interact only through the interface between them

## Slide 21: Layers in practice
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch
Notes: Why go up? Why not stay down in the lower levels?

## Slide 22: Layer encapsulation: Protocol headers
TCP header
IP header
Ethernet
header
HTTP
request/response
User A
User B
Notes: Deepest level most header

## Slide 23: IP is the narrow waist of the layering hourglass
SMTP
HTTP
TCP
UDP
IP
PPP
FDDI
Ethernet
PSTN
Radio
Copper
Optical
NTP
DNS

## Slide 24: Topics
Basics (lectures 1–2)
Application layer (lectures 3–5)
  HTTP, DNS, CDN, Video Streaming, and Cloud
Transport layer (lectures 6–9)
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only

## Slide 25: Hyper Text Transfer Protocol (HTTP)
Client-server architecture
  Server is “always on” and “well known”
  Clients initiate contact to server
Synchronous request/reply protocol
  Runs over TCP, Port 80
Stateless
ASCII format
  Before HTTP/2

## Slide 26: Object request response time
RTT (round-trip time)
  Time for a small packet to travel from client to server and back
Response time
  1 RTT for TCP setup
  1 RTT for HTTP request and first few bytes
  Transmission time
  Total = 2RTT + Transmission Time
Client
Server
TCP syn
TCP syn + ack
TCP ack + HTTP GET
RTT
RTT
Tx

## Slide 27: Improving HTTP performance
Optimizing connections using three “P”s
  Persistent connections
  Parallel/concurrent connections
  Pipelined transfers over the same connection
Caching
  Forward proxy: close to clients
  Reverse proxy: close to servers
Replication

## Slide 28: Scorecard: Getting n small objects
Time dominated by latency
One-at-a-time: ~2n RTT
m concurrent: ~2[n/m] RTT
Persistent: ~ (n+1) RTT
Pipelined: ~2 RTT
Pipelined and Persistent: ~2 RTT first time; RTT later for another n from the same site

## Slide 29: Scorecard: Getting n large objects each of size F
Time dominated by TCP throughput BC (<= BL), where bottleneck link bandwidth is BL
  Assuming all TCP connections go through the same bottleneck link
One-at-a-time: ~ nF/BC
m concurrent: ~ nF/(mB’C)
  Assuming each TCP connection gets the same throughput (B’C), where mB’C <= BL
Pipelined and/or persistent: ~ nF/BC
  The only thing that helps is higher throughput

## Slide 30: Content Distribution Networks (CDN)
Caching and replication as a service
Combination of caching and replication
  Pull: Direct result of clients’requests (caching)
  Push: Expectation of high access rate (replication)

## Slide 31: Hierarchies in the DNS
Three intertwined hierarchies
  Hierarchical namespace
    As opposed to flat namespace
  Hierarchically administered
    As opposed to centralized
  (Distributed) hierarchy of servers
    As opposed to centralized storage

## Slide 32: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers

## Slide 33: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 34: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 35: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 36: Name resolution: Recursive
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 37: Name resolution: Iterative
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?

## Slide 38: DNS caching
Performing all these queries takes time
  Up to 1-second latency before starting download
Caching can greatly reduce overhead
  The top-level servers very rarely change
  Popular sites (e.g., www.google.com) visited often
  Local DNS server often has the information cached
How DNS caching works
  DNS servers cache responses to queries
  Responses include a “time to live” (TTL) field
  Server deletes cached entry after TTL expires

## Slide 39: 5-minute break!

## Slide 40: Announcements
Please fill up midterm teaching evaluation

## Slide 41: HTTP streaming
Video is stored at an HTTP server with a URL
Clients send a GET request for the URL
Server sends the video file as a stream
Client first buffers for a while to minimize interruptions later
Once the buffer reaches a threshold
  The video plays in the foreground
  More frames are downloaded in the background

## Slide 42: DASH : Dynamic Adaptive Streaming over HTTP
Keep multiple resolutions of the same video
  Stored in a manifest file in the HTTP server
Client asks for the manifest file first to learn about the options
Asks for chunks at a time and measures available bandwidth while they are downloaded
  Low bandwidth ⇒ switch to lower bitrate
  High bandwidth ⇒ switch to higher bitrate

## Slide 43: Applications
Common theme: parallelism
  Applications decomposed into tasks
  Running in parallel on different machines
Two common paradigms
  Partition-Aggregate
  Map-Reduce

## Slide 44: Traditional datacenter networks
Rack
Aggregation
Core

## Slide 45: Challenges
Not enough bandwidth
  Oversubscription: Less bandwidth in the ToR-Agg links than all the servers’ bandwidth in the rack
  Oversubscription ratio: Ratio between bandwidth underneath and bandwidth above
Not enough paths between server pairs
  Load balancing issues
  Failure recovery issues

## Slide 46: Modern datacenter networks: More bandwidth, more paths
Rack
Aggregation
Core

## Slide 47: Clos topology
Multi-stage network
k pods, where each pod has two layers of k/2 switches
  k/2 ports up and k/2 down
All links have the same b/w
At most k3/4 machines
Example
  k = 4
  16 machines
For k=48, 27648 machines
Pod 1
Pod 2
Pod 3
Pod 4

## Slide 48: Topics
Basics (lectures 1–2)
Application layer (lectures 3–5)
  HTTP, DNS, CDN, Video Streaming, and Cloud
Transport layer (lectures 6–9)
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only

## Slide 49: Role of the transport layer
(1) Communication between application processes
  Mux and demux from/to application processes
  Implemented using ports
(2) Provide common end-to-end services for app layer
  Reliable, in-order data delivery
  Well-paced data delivery

## Slide 50: UDP vs. TCP
 | UDP | TCP
Data abstraction | Packets (datagrams) | Stream of bytes of arbitrary length
Service | Best-effort (same as IP) | Reliability In-order delivery Congestion control Flow control
  Both UDP and TCP perform mux/demux via ports

## Slide 51: Reliable transport: General concepts
Checksums (for error detection)
Timers (for loss detection)
Acknowledgments (feedback from receiver)
  Cumulative: “received everything up to X”
  Selective: “received X”
Sequence no (detect duplicates, accounting)
Sliding windows (for efficiency)
You should know:
what these concepts are
why they exist
how TCP uses them

## Slide 52: Designing a reliable transport protocol
Stop and wait is correct but inefficient
  Works packet by packet (of size DATA)
  Throughput is (DATA/ RTT)
Sliding window: use pipelining to increase throughput
  n packets at a time results in higher throughput
  MIN(n*DATA/RTT, Link Bandwidth)

## Slide 53: The TCP abstraction
TCP delivers a reliable, in-order, byte stream
Reliable: TCP resends lost packets (recursively)
  Until it gives up and shuts down connection
In-order: TCP only hands consecutive chunks of data to application
Byte stream: TCP assumes there is an incoming stream of data, and attempts to deliver it to app

## Slide 54: Things to know about TCP
How TCP achieves reliability
RTT estimation
Connection establishment/teardown
Flow Control
Congestion Control (concepts only)
For each, know how the functionality is implemented and why it is needed

## Slide 55: Reliability
Having TCP take care of it simplifies application development
How
  Checksums and timers (for error and loss detection)
  Fast retransmit (to detect faster-than-timeout loss)
  Cumulative ACKs (receiver feedback: what’s lost?)
  Sliding windows (for efficiency)
  Buffers at sender (hold packets until ACKs arrive)
  Buffers at receiver (to reorder packets before delivery to application)

## Slide 56: Establishing/terminating a TCP connection
Three-way handshake to establish connection
  Host A sends a SYN (open; “synchronize sequence numbers”) to host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK to acknowledge the SYN ACK
Three-way handshake to terminate (normal operation)
SYN
SYN ACK
ACK
A
B
Data
Data

## Slide 57: Flow control
Why?
  TCP at the receiver must buffer a packet until all packets before it (in byte-order) have arrived and the receiving application has consumed available bytes
  Hence, receiver advances its window when the receiving application consumes data
  Sender advances its window when new data ACK’d
  Risk of sender overrunning the receiver’s buffers
How?
  “Advertised Window” field in TCP header

## Slide 58: Congestion control
Why?
  Because the network itself can be the bottleneck
  Should make efficient use of available network capacity
    While sharing available capacity fairly with other flows
    And adapting to changes in available capacity
How?
  Dynamically adapts the size of the sending window

## Slide 59: Put together
Flow Control
  Restrict window to RWND to make sure that the receiver isn’t overwhelmed
Congestion Control
  Restrict window to CWND to make sure that the network isn’t overwhelmed
Together
  Restrict window to min{RWND, CWND} to make sure that neither the receiver nor the network are overwhelmed

## Slide 60: CC implementation
States at sender
  CWND (initialized to a small constant)
  ssthresh (initialized to a large constant)
  dupACKcount and timer
Events
  ACK (new data)
  dupACK (duplicate ACK for old data)
  Timeout

## Slide 61: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
CWND packets per RTT
Hence, after one RTT with no drops: CWND = 2xCWND

## Slide 62: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
Else
  CWND = CWND + 1/CWND
Slow start phase
CWND packets per RTT
Hence, after one RTT with no drops: CWND = CWND + 1
Congestion avoidance phase

## Slide 63: Event: TimeOut
On Timeout
  ssthresh  CWND/2
  CWND  1

## Slide 64: Event: dupACK
dupACKcount ++
If dupACKcount = 3 /* fast retransmit */
  ssthresh = CWND/2
  CWND = CWND/2

## Slide 65: Example
t
Window
Slow-start restart: Go back to CWND = 1 MSS, but take advantage of knowing the previous value of CWND
Slow start in operation until it reaches half of previous CWND, i.e., SSTHRESH
Timeout
Fast Retransmission
SSThresh
Set to Here

## Slide 66: TCP flavors
TCP-Tahoe
  CWND =1 on 3 dupACKs
TCP-Reno
  CWND =1 on timeout
  CWND = CWND/2 on 3 dupACKs
TCP-newReno
  TCP-Reno + improved fast recovery
TCP-SACK
  Incorporates selective acknowledgements

## Slide 67: A simple model for TCP throughput
A
Loss
time
cwnd
1
RTT
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 68: A simple model for TCP throughput
in MSS
A
Loss
time
cwnd
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 69: Summary
Practice Exams on GitHub