## Slide 1: EECS 489 Computer Networks Winter 2025
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
TCP flow control
TCP congestion control

## Slide 3: RFC 675 ($4.3.2)

## Slide 4: TCP state transitions
Data, ACK exchanges are in here

## Slide 5: TCP client lifecycle
CLOSED
SYN_SENT
ESTABLISHED
FIN_WAIT_1
FIN_WAIT_2
TIME_WAIT
Send SYN
Receive SYN-ACK
Send ACK
Send FIN
Receive ACK
Send Nothing
Receive FIN
Send ACK
Wait 30 sec

## Slide 6: TCP server lifecycle
CLOSED
LISTEN
SYN_RCVD
ESTABLISHED
CLOSE_WAIT
LAST_ACK
Create a listen socket
Receive SYN
Send SYN-ACK
Receive ACK
Send Nothing
Receive FIN
Send ACK
Send FIN
Receive ACK
Send Nothing

## Slide 7: TCP Flow Control

## Slide 8: Recap: Sliding window
Both sender and receiver maintain a window
Left edge of window:
  Sender: beginning of unacknowledged data
  Receiver: beginning of expected data
    First “gap” in received data
    When sender gets ack, knows that receiver’s window has moved
Right edge: Left edge + constant
  The constant is only limited by buffer size in the transport layer
Notes: Picture on board

## Slide 9: Sliding window at sender
Sending process
First unACKed byte
Last byte can send
TCP
Last byte written
Previously
ACKed bytes
Buffer size (B)

## Slide 10: Sliding window at receiver
Receiving process
Next byte needed (1st byte not received)
Last byte read
Last byte received
Received and ACKed
Buffer size (B)
Sender might overrun the receiver’s buffer

## Slide 11: Solution: Advertised window (Flow Control)
Receiver uses an “Advertised Window” (RWND) to prevent sender from overflowing its window
  Receiver indicates value of RWND in ACKs
  Sender ensures that the total number of bytes in flight <= RWND

## Slide 12: TCP header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Data

## Slide 13: Sliding window at receiver
Receiving process
Next byte needed (1st byte not received)
Last byte read
Last byte received
Buffer size (B)
RWND = B - (LastByteReceived - LastByteRead)

## Slide 14: Sliding window at sender
Sending process
First unACKed byte
Last byte can send
TCP
Last byte written
RWND

## Slide 15: Sliding window with flow control
Sender: window advances when new data ACK’d
Receiver: window advances as receiving process consumes data
Receiver advertises to the sender where the receiver window currently ends (“righthand edge”)
  Sender agrees not to exceed this amount
UDP does not have flow control
  Data can be lost due to buffer overflow

## Slide 16: Advertised window limits rate
Sender can send no faster than RWND/RTT bytes/sec
Receiver only advertises more space when it has consumed old arriving data
What happens when RWND=0?
  Sender keeps probing with one data bytes
In original TCP design, that was the sole protocol mechanism controlling sender’s rate
  What’s missing?

## Slide 17: TCP Congestion Control

## Slide 18: What is congestion?
If two packets arrive at a router at the same time
  Router will transmit one and buffer/drop the other
Internet traffic is bursty
  Many packets can arrive close in time
  Causes packet delays and drops
Root cause: statistical multiplexing

## Slide 19: Congestion collapse in 1980s
Sending rate only limited by flow control
  Dropped packets  senders (repeatedly!) retransmit
Led to “congestion collapse” in Oct. 1986
  Throughput on the NSF network dropped from 32Kbits/s to 40bits/sec
“Fixed” by Van Jacobson’s development of TCP’s congestion control (CC) algorithms

## Slide 20: Jacobson’s fix to TCP
Extend TCP’s existing window-based protocol but adapt the window size in response to congestion
A pragmatic and effective solution
  Required no upgrades to routers or applications!
  Patch of a few lines of code to TCP implementations
Extensively researched and improved upon
  Especially now with datacenters and cloud services

## Slide 21: Key design considerations
How do we know the network is congested?
  Implicit and/or explicit signals from the network
Who takes care of congestion?
  End hosts (may receive some help from the network)
How do we handle congestion?
  Continuous adaptation

## Slide 22: Three issues to consider
Discovering the available (bottleneck) bandwidth
Adjusting to variations in bandwidth
Sharing bandwidth between flows

## Slide 23: Abstract view
Ignore internal structure of router and model it as a single queue for a particular input-output pair
Sending Host
Buffer in Router
Receiving Host
A
B

## Slide 24: Discovering available bandwidth
Pick sending rate to match bottleneck bandwidth
  Without any a priori knowledge
  Could be gigabit link, could be a modem
100 Mbps
Sending Host
Buffer in Router
Receiving Host
A
B

## Slide 25: Adjusting to variations in bandwidth
Adjust rate to match instantaneous bandwidth
  Assuming you have rough idea of bandwidth
A
B
BW(t)

## Slide 26: Multiple flows and sharing bandwidth
Two Issues:
  Adjust total sending rate to match bandwidth
  Allocation of bandwidth between flows
A2
B2
BW(t)
A1
A3
B3
B1

## Slide 27: Reality
Congestion control is a resource allocation problem involving many flows, many links, and complicated global dynamics
1Gbps
600Mbps
1Gbps

## Slide 28: Possible approaches
(0) Send without care
  Many packet drops

## Slide 29: Possible approaches
(0) Send without care
(1) Reservations
  Pre-arrange bandwidth allocations
  Requires negotiation before sending packets
  Low utilization

## Slide 30: Possible approaches
(0) Send without care
(1) Reservations
(2) Pricing
  Don’t drop packets for the high-bidders
  Requires payment model

## Slide 31: Possible approaches
(0) Send without care
(1) Reservations
(2) Pricing
(3) Dynamic Adjustment
  Hosts infer level of congestion; adjust
  Network reports congestion level to hosts; hosts adjust
  Combinations of the above
  Simple to implement but suboptimal, messy dynamics

## Slide 32: Possible approaches
(0) Send without care
(1) Reservations
(2) Pricing
(3) Dynamic Adjustment
Generality of dynamic adjustment has proven to be very powerful
  Doesn’t presume business model, traffic characteristics, application requirements
  But does assume good citizenship!

## Slide 33: 5-minute break!

## Slide 34: TCP’s approach in a nutshell
Each TCP connection has a window
  Controls number of packets in flight
Sending rate ~Window/RTT
Vary window size to control sending rate

## Slide 35: Windows to keep in mind
Congestion Window: CWND
  Bytes that can be sent without overflowing routers
  Computed by sender using congestion control algo.
Flow control window: RWND
  Bytes that can be sent without overflowing receiver
  Determined by the receiver and reported to the sender
Sender-side window = min {CWND, RWND}
  Assume for this lecture that RWND >> CWND

## Slide 36: Note
This lecture talks about CWND in units of MSS
  MSS (Maximum Segment Size): the amount of payload data in a TCP packet
  This is only for the simplicity of presentation
Real implementations maintain CWND in bytes

## Slide 37: Two basic questions
How does the sender detect congestion?
How does the sender adjust its sending rate?
  To address three issues
    Finding available bottleneck bandwidth
    Adjusting to bandwidth variations
    Sharing bandwidth

## Slide 38: Detecting congestion
Packet delays
  Tricky: noisy signal (delay often varies considerably)
Routers tell end hosts when they’re congested
Packet loss
  Fail-safe signal that TCP already has to detect
  Complication: non-congestive loss (e.g., checksum errors)

## Slide 39: Not all losses are the same
Duplicate ACKs: isolated loss
  Still getting ACKs
Timeout: much more serious
  Not enough dupacks
  Must have suffered several losses
Will adjust rate differently for each case

## Slide 40: Rate adjustment
Basic structure
  Upon receipt of ACK (of new data): increase rate
  Upon detection of loss: decrease rate
How we increase/decrease the rate depends on the phase of congestion control we’re in:
  Discovering available bottleneck bandwidth vs.
  Adjusting to bandwidth variations

## Slide 41: Bandwidth discovery with “Slow Start”
Goal: estimate available bandwidth
  Start slow (for safety)
  Ramp up quickly (for efficiency)
Consider
  RTT = 100ms, MSS=1000bytes
  Window size to fill 1Mbps of BW = 12.5 packets
  Window size to fill 1Gbps = 12,500 packets
  Either is possible!

## Slide 42: Slow Start phase
Sender starts at a slow rate, but increases exponentially until first loss
Start with a small congestion window
  Initially, CWND = 1
  So, initial sending rate is MSS/RTT
Double the CWND for each RTT with no loss
Notes: MSS vs MTU??

## Slide 43: Slow Start in action
For each RTT: double CWND
  i.e., for each ACK, CWND += 1
Linear increase per ACK(CWND+1)  exponential increase per RTT (2*CWND)

## Slide 44: Slow Start in action
For each RTT: double CWND
  i.e., for each ACK, CWND += 1
D
A
D
D
A
A
D
D
Src
Dest
D
D
1
2
4
3
A
A
A
A
8

## Slide 45: When does Slow Start stop?
Slow Start gives an estimate of available bandwidth
  At some point, there will be loss
Introduce a “slow start threshold” (ssthresh)
  Initialized to a large value
If CWND > ssthresh, stop Slow Start

## Slide 46: Adjusting to varying bandwidth
CWND > ssthresh
  Stop rapid growth and focus on maintenance
Now, want to track variations in this available bandwidth, oscillating around its current value
  Repeated probing (rate increase) and backoff (decrease)
TCP uses: “Additive Increase Multiplicative Decrease” (AIMD)

## Slide 47: AIMD
Additive increase
  For each ACK, CWND = CWND+ 1/CWND
  CWND is increased by one only if all segments in a CWND have been acknowledged
Multiplicative decrease
  On packet loss, divide ssthresh in half and slow start
    ssthresh = CWND/2
    CWND = 1
    Initiate Slow Start
  Note that we’re ignoring the “dupAck” fix for now

## Slide 48: AIMD leads to TCP sawtooth
Loss
Exponential “slow start”
t
Window
Multiplicative Decrease
Additive Increase

## Slide 49: Why AIMD?
Recall the three issues
  Finding available bottleneck bandwidth
  Adjusting to bandwidth variations
  Sharing bandwidth
Two goals for bandwidth sharing
  Efficiency: High utilization of link bandwidth
  Fairness: Each flow gets equal share

## Slide 50: Why AIMD?
Every RTT, we can do
  Multiplicative increase or decrease: CWND a*CWND
  Additive increase or decrease: CWND CWND + b
Four alternatives:
  AIAD: gentle increase, gentle decrease
  AIMD: gentle increase, drastic decrease
  MIAD: drastic increase, gentle decrease
  MIMD: drastic increase and decrease

## Slide 51: Simple model of congestion control
Two users
  rates x1 and x2
Congestion when x1+x2 > 1
Unused capacity when x1+x2 < 1
Fair when x1 =x2
User 1’s rate (x1)
User 2’s rate (x2)
Fairness line (x1 =x2)
Efficiency line (x1+x2 = 1)
1
1
congested 
 inefficient

## Slide 52: Example
User 1: x1
User 2: x2
Fairness
line
Efficiency
line
1
1
Inefficient: x1+x2=0.7
(0.2, 0.5)
Congested: x1+x2=1.2
(0.7, 0.5)
Efficient: x1+x2=1
Fair
(0.5, 0.5)
congested 
 inefficient
Efficient: x1+x2=1
Not fair
(0.7, 0.3)

## Slide 53: AIAD
Increase: x + aI
Decrease: x - aD
Does not converge to fairness
(x1,x2)
(x1-aD,x2-aD)
(x1-aD+aI), x2-aD+aI))
congested 
 inefficient
Fairness
line
Efficiency
line
User 1: x1
User 2: x2

## Slide 54: AIAD Sharing Dynamics
A
B
x1
D
E
x2

## Slide 55: MIMD
Increase: x*bI
Decrease: x*bD
Does not converge to fairness
(x1,x2)
(bdx1,bdx2)
(bIbDx1, bIbDx2)
congested 
 inefficient
Fairness
line
Efficiency
line
User 1: x1
User 2: x2

## Slide 56: AIMD
(bDx1+aI, bDx2+aI)
Increase: x+aI
Decrease: x*bD
Converges to fairness
(x1,x2)
(bDx1,bDx2)
congested 
 inefficient
Fairness
line
Efficiency
line
User 1: x1
User 2: x2

## Slide 57: AIMD Sharing Dynamics
A
50 packets/sec
B
x1
D
E
Rates equalize  fair share
x2

## Slide 58: MIAD
Increase: x*bI
Decrease: x - aD
Does not converge to fairness
Does not converge to efficiency
“Analysis of the Increase and Decrease Algorithms for Congestion Avoidance in Computer Networks”
  -- Chiu and Jain
(x1h,x2h)
(x1h-aD,x2h-aD)
(bI(x1h-aD), bI(x2h-aD))
Fairness
line
Efficiency
line
User 1: x1
User 2: x2

## Slide 59: Summary
Flow control ensures that the sender does not overflow the receiver
Congestion control ensures that the sender does not overflow the network
  Discover bandwidth
  Adjust to conditions
  Share bandwidth with others