## Slide 1: EECS 489 Computer Networks Winter 2017
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
Video streaming
Datacenter applications

## Slide 3: Recap: Web components
Infrastructure:
  Clients
  Servers (DNS, CDN, Datacenters)
Content:
  URL: naming content
  HTML: formatting content
Protocol for exchanging information: HTTP

## Slide 4: Recap: HTTP
Client-server architecture
  Server is “always on” and “well known”
  Clients initiate contact to server
Synchronous request/reply protocol
  Runs over TCP, Port 80
Stateless
ASCII format
  Before HTTP/2

## Slide 5: Recap: CDN
Caching and replication as a service
Large-scale distributed storage infrastructure (usually) administered by one entity
  e.g., Akamai has servers in 20,000+ locations
Combination of caching and replication
  Pull: Direct result of clients’requests (caching)
  Push: Expectation of high access rate (replication)
Can do some processing to handle dynamic webpage content
Notes: Transcoding = change compression rate per user’s bandwidth

## Slide 6: Recap: DNS
Resolve names to addresses
  Uniqueness: no naming conflicts
  Scalable: many names and frequent updates
  Distributed, autonomous administration
    Ability to update my own (machines’) names
    Don’t have to track everybody’s updates
  Highly available
  Lookups are fast
Level of indirection

## Slide 7: Putting it all together
User
Server
HTTP GET

## Slide 8: Putting it all together
User
Server
HTTP Response
<html>
<body>
... …
</body>
</html>

## Slide 9: Putting it all together
User
Server
<html>
<body>
<img />
</body>
</html>
DNS Server
CDN Server - 1
CDN Server - 2
HTTP GET

## Slide 10: Putting it all together
User
Server
<html>
<body>
<img />
</body>
</html>
DNS Server
CDN Server - 1
CDN Server - 2
HTTP Response

## Slide 11: How is video different?
Often too large to send in one GET
Doesn’t even make sense even if its possible
  Users may skip forward! ⇒ save bandwidth wastage
  Users connection quality may change (e.g., switching from WiFi to LTE) ⇒ lower resolution to save bandwidth
Our focus is on stored video (i.e., not live)

## Slide 12: Why video is important?
Dominates the Internet traffic landscape
  About every 2 of 3 bytes!
Residential ISP traffic share of video content providers
  Netflix: 37%
  YouTube: 16%
  Overall: ~70%

## Slide 13: The video medium
Video is a sequence of images/frames displayed at a constant rate (moving pictures)
Digital image is an array of pixels, each pixel represented by bits
Examples:
  Single frame image encoding: 1024x1024 pixels, 24 bits/pixel ⇒ 3 MB/image
  Movies: 24 frames/sec ⇒ 72 MB/sec
  TV: 30 frames/sec ⇒ 90 MB/sec

## Slide 14: The video medium (cont’d)
Compression is key
  Lots of algorithms to compress
The same video can be (and typically is) compressed to multiple quality levels
  E.g., 480p, 720p, 1080p, 4K
Why multiple resolutions?
  Adapt to conditions

## Slide 15: How do we serve video?
It’s in the name!
  Video streaming

## Slide 16: HTTP streaming
Video is stored at an HTTP server with a URL
Clients send a GET request for the URL
Server sends the video file as a stream
Client first buffers for a while. Why?
  To minimize interruptions later
Once the buffer reaches a threshold
  The video plays in the foreground
  More frames are downloaded in the background

## Slide 17: HTTP streaming
video
recorded (e.g., 30 frames/sec)
2. video
sent
Cumulative data
streaming: at this time, client
playing out early part of video,
while server still sending later
part of video
network delay
(fixed in this example)
time
3. video received,
played out at client
(30 frames/sec)

## Slide 18: Challenges
Absorb network delay variations
Handle user interactions
  Jump forward, fast-forward, rewind, pause
Handle packet loss, retransmission etc.

## Slide 19: HTTP streaming: Revisited
constant bit
rate video
transmission
Cumulative data
time
variable
network
delay
client video
reception
constant bit
rate video
playout at client
client playout
delay
buffered
video
Client-side buffering and playout delay: compensate for network-added delay, delay jitter

## Slide 20: Issues with HTTP streaming
Same bitrate for all clients
  Clients can have very different network conditions
  Clients network conditions can change over time
Cannot dynamically adapt to conditions

## Slide 21: DASH : Dynamic Adaptive Streaming over HTTP
Keep multiple resolutions of the same video
  Stored in a manifest file in the HTTP server
Client asks for the manifest file first to learn about the options
Asks for chunks at a time and measures available bandwidth while they are downloaded
  Low bandwidth ⇒ switch to lower bitrate
  High bandwidth ⇒ switch to higher bitrate

## Slide 22: 5-minute break!

## Slide 23: Announcements
Assignment 1 is due tonight!
Assignment 2 will be out next week

## Slide 24: Who’s serving Web services?
User
Server
HTTP GET

## Slide 25: Who’s serving Web services?
User
Server
HTTP Response
<html>
<body>
... …
</body>
</html>

## Slide 26: Who’s serving Web services? Datacenters
Source: Google

## Slide 27: Who’s serving Web services? Datacenters
Source: Google

## Slide 28: Who’s serving Web services? Datacenters
Source: Facebook

## Slide 29: Datacenter networks
Tens to hundreds of thousands of hosts, often closely coupled, in close proximity:
  E-commerce (e.g., Amazon)
  Content servers (e.g., NetFlix, YouTube, Apple, Microsoft)
  Search engines, data mining (e.g., Google)
  Social networks (e.g., Facebook, Twitter, Instagram)
Challenges:
  Multiple applications, each serving massive numbers of clients

## Slide 30: How big exactly?
1M servers/site [Microsoft/Amazon/Google]
> $1B to build one site [Facebook]
>$20M/month/site operational costs [MS’09]
Data center hardware spending will grow to $177 billion in 2017. [Gartner report]
But only O(10-100) sites

## Slide 31: Datacenter networks
Server
ToR Switch
Aggregation

## Slide 32: Datacenter networks (Cont.)
Rack
Aggregation
Core

## Slide 33: Challenges
Not enough bandwidth
  Oversubscription: Less bandwidth in the ToR-Agg links than all the servers bandwidth in the rack
  Oversubscription ratio: Ratio between bandwidth underneath and bandwidth above
Not enough paths between server pairs
  Load balancing issues
  Failure recovery issues

## Slide 34: Modern datacenter networks: More bandwidth, more paths
Rack
Aggregation
Core

## Slide 35: Let’s take a Web service
Mosharaf

## Slide 36: Who’s serving Web services?
Rack
Aggregation
Core

## Slide 37: What happens inside?
Mosharaf
Top-level Aggregator
Mid-level Aggregators
Workers

## Slide 38: Partition-Aggregate traffic
Mosharaf
Top-level Aggregator
Mid-level Aggregators
Workers

## Slide 39: Partition-Aggregate traffic
Rack
Aggregation
Core
North-South Traffic
East-West Traffic

## Slide 40: End-to-end response time
Less than 200 milliseconds between receiving user query in the browser and displaying the results
  RTT = O(10) to 100 milliseconds
  What remains?
Next time, when the page is not loading fast enough, think about the poor servers working for you 

## Slide 41: Summary
Video streaming
  Too large to send as a whole, so stream it
  Dynamically adapt to the network and users
Cloud applications
  Forms the backend of modern web services
  Where all the processing happens
Next lecture
  Read 3.1 to 3.5 of K&R