## Slide 1: EECS 489 Computer Networks Winter 2017
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
Datacenter applications
Datacenter topologies

## Slide 3: Datacenters run the world
Source: Google

## Slide 4: Datacenters run the world
Source: Google

## Slide 5: Datacenters run the world
Source: Facebook

## Slide 6: How much power is needed?
0.0003 kWh to answer a typical Google search
  0.05 kW to use a laptop for an hour
  0.1 kW to run a ceiling fan for an hour
  1.1 kW to use a coffee maker for an hour
How much power is 30 MW?
  6,000 average homes with central air (~5 kW/home)
  300 fast food restaurants
  45 large retail stores
  1.5 Sears Towers
  1 datacenter

## Slide 7: How big is a datacenter (DC)?
1M servers/site [Microsoft/Amazon/Google]
> $1B to build one site [Facebook]
>$20M/month/site operational costs [MS’09]
Data center hardware spending will grow to $177 billion in 2017. [Gartner report]
But only O(10-100) sites

## Slide 8: Implications (1)
Scale
  Need scalable designs: e.g., avoid flooding
  Low-cost designs: e.g., use commodity technology
  High utilization (efficiency): e.g., >80% avg. utilization
    Contrast: avg. utilization on Internet links often ~30%
  Tolerate frequent failure
    Large number of (low cost) components
  Automate

## Slide 9: Implications (2)
Service model: clouds / multi-tenancy
  Performance guarantees
  Isolation guarantees
  Portability

## Slide 10: Applications
Common theme: parallelism
  Applications decomposed into tasks
  Running in parallel on different machines
Two common paradigms
  Partition-Aggregate
  Map-Reduce

## Slide 11: Partition-Aggregate
Mosharaf
Top-level Aggregator
Mid-level Aggregators
Workers

## Slide 12: Partition-Aggregate
Mosharaf
Top-level Aggregator
Mid-level Aggregators
Workers

## Slide 13: Map-Reduce
Reduce Stage
Map Stage
The most popular software that follows this paradigm is Apache Spark

## Slide 14: Datacenter networks
Server
ToR Switch
Aggregation

## Slide 15: Datacenter networks (Cont.)
Rack
Aggregation
Core

## Slide 16: Datacenter traffic
Rack
Aggregation
Core
North-South Traffic
East-West Traffic

## Slide 17: East-West traffic
Traffic between servers in the datacenter
Communication within “big data” computations
Traffic may shift on small timescales (< minutes)

## Slide 18: Datacenter traffic characteristics
Two key characteristics
  Most flows are small
  Most bytes come from large flows
Applications want
  High bandwidth (large flows)
  Low latency (small flows)

## Slide 19: High bandwidth
Ideal: Each server can talk to any other server at its full access link rate
Conceptually: Datacenter network as one giant switch

## Slide 20: Datacenter network as one giant switch

## Slide 21: Datacenter network as one giant switch

## Slide 22: Datacenter network as one giant switch
One
GIANT
Switch

## Slide 23: High bandwidth
Ideal: Each server can talk to any other server at its full access link rate
Conceptually: Datacenter network as one giant switch
  Would require a 10 Pbits/sec switch!
    1M ports (one port/server)
    10Gbps per port
Practical approach: build a network of switches (“fabric”) with high “bisection bandwidth”
  Each switch has practical #ports and link speeds

## Slide 24: Bisection bandwidth
Partition a network into two equal parts
Minimum bandwidth between the partitions is the bisection bandwidth
Full bisection bandwidth: bisection bandwidth in an N node network is N/2 times the bandwidth of a single link
  Nodes of any two halves can communicate at full speed with each other

## Slide 25: Achieving full bisection bandwidth
Scale up
  Make links fatter toward the core of the network
Problem: Scaling up a traditional tree topology is expensive!
  Requires non-commodity / impractical / link and switch components
Solutions?
  Over-subscribe (i.e., provision less than full BBW)
  Better topologies

## Slide 26: Oversubscription
Need techniques to avoid congesting oversubscribed links!
10G
20G
40G
10G
10G
20G

## Slide 27: Oversubscription
Not enough bandwidth
  Oversubscription: Less bandwidth in the ToR-Agg links than all the servers bandwidth in the rack
  Oversubscription ratio: Ratio between bandwidth underneath and bandwidth above
Not enough paths between server pairs
  Load balancing issues
  Failure recovery issues

## Slide 28: Better topologies
Rack
Aggregation
Core

## Slide 29: Better topologies
Rack
Aggregation
Core

## Slide 30: Clos topology
Multi-stage network
k pods, where each pod has two layers of k/2 switches
  k/2 ports up and k/2 down
All links have the same b/w
At most k3/4 machines
Example
  k = 4
  16 machines
For k=48, 27648 machines
Pod 1
Pod 2
Pod 3
Pod 4

## Slide 31: Challenges in scale-out designs?
Topology offers high bisection bandwidth
All other system components must be able to exploit this available capacity
  Routing must use all paths
  Transport protocol must fill all pipes (fast)

## Slide 32: 5-minute break!

## Slide 33: Datacenter traffic characteristics
Two key characteristics
  Most flows are small
  Most bytes come from large flows
Applications want
  High bandwidth (large flows)
  Low latency (small flows)

## Slide 34: Very low RTTs within the DC
Implications of O(1) μsec latency
  BW x delay
    10Gbps x 1μsec = 10000 bits = 2.5 500-Byte packets
  Consider TX 500B @ 10Gbps = 0.4μs per hop = 2μs if a packet traverses 5 hops and waits behind one packet at every hop
  What does this mean for buffering and switch design?
  What does this mean for congestion control?

## Slide 35: Application-level latency requirements
Applications want low latency
  Predictable / guaranteed bounds on flow completion time, including the worst-case!
  How is still an open question

## Slide 36: What’s different about DC networks?
Characteristics
  Huge scale
    ~20,000 switches/routers
    Contrast: AT&T ~500 routers

## Slide 37: What’s different about DC networks?
Characteristics
  Huge scale
  Limited geographic scope
    High bandwidth: 10/40/100G (Contrast: DSL/WiFi)
    Very low RTT: 1-10s μsecs (Contrast: 100s msecs)

## Slide 38: What’s different about DC networks?
Characteristics
  Huge scale
  Limited geographic scope
  Limited heterogeneity
    Link speeds, technologies, latencies, …

## Slide 39: What’s different about DC networks?
Characteristics
  Huge scale
  Limited geographic scope
  Limited heterogeneity
  Regular/planned topologies (e.g., trees)
    Contrast: ad-hoc evolution of wide-area topologies

## Slide 40: What’s different about DC networks?
Goals
  Extreme bisection bandwidth requirements
    Recall that all east-west traffic use it
    Target: any server can communicate at its full link speed
    Target: making impactful use of this bandwidth by leveraging application-level knowledge
    How: Next lecture

## Slide 41: What’s different about DC networks?
Goals
  Extreme bisection bandwidth requirements
  Extreme latency requirements
    Affects user-facing applications
    Target: 1μs RTTs
    Target: Minimize flow completion time
    How: Next lecture

## Slide 42: What’s different about DC networks?
Goals
  Extreme bisection bandwidth requirements
  Extreme latency requirements
  Predictable, deterministic performance
    “Your packet will reach in Xms, or not at all”
    “Your VM will always see at least YGbps throughput”
    How: Still an open question

## Slide 43: What’s different about DC networks?
Goals
  Extreme bisection bandwidth requirements
  Extreme latency requirements
  Predictable, deterministic performance
  Differentiating between tenants is key
  “No traffic between VMs of tenant A and tenant B”
  “Tenant X cannot consume more than XGbps”
  “Tenant Y’s traffic is low priority”
  How: Mechanism can be SDN, but there are many policies without any consensus

## Slide 44: What’s different about DC networks?
Goals
  Extreme bisection bandwidth requirements
  Extreme latency requirements
  Predictable, deterministic performance
  Differentiating between tenants is key
  Scalability

## Slide 45: What’s different about DC networks?
Goals
  Extreme bisection bandwidth requirements
  Extreme latency requirements
  Predictable, deterministic performance
  Differentiating between tenants is key
  Scalability
  Cost/efficiency
    Focus on commodity solutions, ease of management

## Slide 46: What’s different about DC networks?
New degrees of (design) freedom
  Single administrative domain
    Can deviate from standards, invent your own, etc.
    Clean-slate deployment is still feasible

## Slide 47: What’s different about DC networks?
New degrees of (design) freedom
  Single administrative domain
  Control over network and endpoint(s)
    Can change (say) addressing, congestion control, etc.
    Can add mechanisms for security/policy/etc. at the endpoints (typically in the hypervisor)

## Slide 48: What’s different about DC networks?
New degrees of (design) freedom
  Single administrative domain
  Control over network and endpoint(s)
  Control over the placement of traffic source/sink
    Map-Reduce scheduler chooses where tasks run
    Distributed file system dictates where data blocks are replicated
    Can control what traffic crosses which links

## Slide 49: Summary
Datacenters
  New characteristics and goals ⇒ new opportunities
  Scalability is the baseline requirement
  More emphasis on performance, both on bandwidth and latency
  Less emphasis on heterogeneity
  Less emphasis on interoperability
Next lecture: networking in datacenters
Notes: -- incast?
-- one big switch abstraction…